## Slide 1
2020 Postdoc Research Day Presentation Conference.
Design of a Submersible Underwater Capillary Electrophoresis Analytical System
Tomas Drevinskas, Florian Kehl, Konstantin Zamuruyev, Peter A. Willis
Organization: Org#389
Advisor: Dr. Peter A. Willis (Org #389)
Postdoc Program: NPP

## Slide 2
Abstract
Scientists are interested in Ocean worlds because extraterrestrial life might be there. Chemical compounds themselves can hardly be treated as the bio-signature, however, their patterns can. Also, the shift of symmetry in a chirality is considered a distinguished feature that only life has. Enantiomers have the same physicochemical properties, therefore no remote sensing method can be used to detecting them. Contrary, in situ chemical analysis, is a powerful promising approach. Real samples contain a pool of various substances, therefore a separation technique should be used to detect and quantify them. To investigate water in the Ocean world, an analytical method should be capable of aqueous sample analysis. Due to instrumental simplicity, miniaturization, and integration capabilities, the first method of choice is capillary electrophoresis [1].
This work aimed to design a submersible underwater capillary electrophoresis analytical system.
Reference
1. Drevinskas T et al (2020) Complete capillary electrophoresis process on a drone: towards a flying micro-lab. Anal Methods. https://doi.org/10.1039/D0AY01220C
Introduction

## Slide 3
To design such an instrument, several problems have to be overcome:
Sample must be introduced from the outside
The system has to be high-pressure resistant
It must have closed high voltage compartments
It must have a high voltage decoupling mechanism
It has to be completely automated
It must be power efficient
A special format has to be used to ensure the small size
To our knowledge, no such system has been designed yet. Stated problems are not so easy to overcome. Such an instrument will also be useful in chemical oceanography tracking various chemical substances of biotic and abiotic origin.
I am extremely interested in designing automated and autonomous chemical analysis instruments hoping that someday they will be used to answer some important questions or at least will aid in some way.
Problem Description

## Slide 4
Theory: capillary electrophoresis
High voltage
Power supply
Detector
Separation
capillary
Anode
Cathode
Sample
zone
Vials
Chart: Time (s)
Peaks
(detected substances)

## Slide 5
Multiple sub-systems compose an instrument
Fluidic
High Voltage
Pneumatic
Sample Injection
Electronics
Firmware

## Slide 6
Pneumatics: solenoid valve-based pressure and vacuum distribution

## Slide 7
Fluidics: solenoid valve-based fluid distribution

## Slide 8
High Voltage handling
Flat bottom fitting
Bubble trap
Solution reservoid
High Voltage
Electrode
Compartment
Coned capillary fitting
Injector valve
Separation capillary
Ground
HV connection
PTFE Air line
75-100 µm I.D. capillary
50 µm I.D. capillary
inlet
outlet
inlet
outlet
HV decoupling
Air line
HV decoupling
Air line

## Slide 9
Connected sub-systems

## Slide 10
Designed instrument
Battery
Pack
Electronics
Pneumatics

## Slide 11
Designed instrument
Pneumatics
Fluidics
High Voltage
Compartments

## Slide 12
Designed instrument
High Voltage
Compartments
Rotary injection
valve
Solution
reservoirs

## Slide 13
Conditions:
Background electrolyte: 0.5 M acetic acid
Separation voltage: 10 kV
Total length of the capillary 50 cm
Effective length of the capillary 40 cm
Inner diameter of the capillary 50 µm
Injection performed into rotary valve injection cavity using vacuum of 5 psi for 30 seconds
Before analysis, capillary conditioned with water and background electrolyte for 6 minutes each
Actual separations

## Slide 14
Real Sample analysis: washings from the surface of the table
Chart: Original data
Chart: Temperature-compensated data
K+
K+
Ca2+
Ca2+
Na+
Na+

## Slide 15
System optimization
Development of analytical procedure in the laboratory
In situ Applications
Next steps

## Slide 16
Participation in a conference:
36th International Symposium on Microscale Separations and Bioanalysis. September 27-30, virtual edition. Tomas Drevinskas, Florian Kehl, Konstantin Zamuruyev, Aaron Noell, Vlad Cretu, Andrew Demartino, Peter A. Willis. Development of an Underwater Autonomous Capillary Electrophoresis Unit for Potential Future Ocean World Exploration and Terrestrial Chemical Oceanography
I would like to express my gratitude to my scientific advisor Dr. Peter. A. Willis and my Colleagues Dr. Florian Kehl and Dr. Konstantin Zamuruyev for insightful scientific discussions and support. I am also grateful to the whole research group for the support.
© 2020 California Institute of Technology. Government and NASA Postdoctoral Program sponsorship is acknowledged.
Publications and Acknowledgements