## Slide 1
2020 Postdoc Research Day Presentation Conference
Bohoon Kim
Organization: Planetary Mass Spectrometry (389T)
Advisor: Dragan Nikolic and Frank Maiwald
Postdoc Program: JPL Postdoctoral Fellow
A numerical modeling of electrostatic radiation shields

## Slide 2
Introduction – Radiation Sources in Deep Space
Sources: NASA SOHO solar observatory, NASA Hubble and Chandra images
Sources: NASA Langley Research Center
Two types of environment of concern: Galactic Cosmic Radiation (GCR) and Solar Particle Events (SPE)
GCR : Highly charged, energetic protons originating outside the solar system
SPE : Low to medium energy protons associated with coronal mass ejections
Radiation Syndrome

## Slide 3
Objectives
To simulate the motion of charged ions through an arbitrary highly-charged electrostatic shielding system for interplanetary human spaceflight
[ION BEAM Experiment]

## Slide 4
Experimental and Numerical Comparison
[1 Layer at 45 deg : 6 MeV H+]
[-10 kV & +2 kV]
[-50 kV & +30 kV]
Exp.
Cal.
Exp.
Cal.

## Slide 5
Timepix Measurement (pixel particle detector)
Central electrode
[Fluorescent screen]
[Timepix screen]
2 MeV
6 MeV
22.5 MeV
As the voltage increases, ions are gradually pushed to the right, widening the area of the safe zone.

## Slide 6
Shielding Effect
-50kV
50kV
-50kV
[Electrode Array]
[Grid Structure]
-50kV
50kV
-50kV
Grid structure has similar performance as the electrode array but with 3 times lower stored charge, and can be foldable with small transportation volume.
Electrode Array
Grid Structure

## Slide 7
Shielding Effect
Timepix
Position1
Grid
Timepix
Position2
Timepix
Position3
Shielding efficiency of up to 60% was obtained on the timepix screen at the distant position 3. (Dispersion effect of ion beam according to distance)
60%
Ion Beam
Position1
Position2
Position3

## Slide 8
Conclusions – Future work
Van de Graaff generator (up to 5 megavolts)
IONS : 2 MeV H+
+50 kV -50 kV
+500 kV -500 kV
+5000 kV -5000 kV
3D structure to shield all directions
Buckminster-fullerene stacked in two layers