## Slide 1
Onboard Monitoring of Silver Biocide during Future Human Space Exploration Missions
Mauro S. Ferreira Santos
Organization: 389U
Advisor: Maria Fernanda Mora (389U)
Postdoc Program: JPL

## Slide 2
To extend human presence deeper into space is one of NASA's goals;
Water is a key resource to enable long duration human space travel;
On the International Space Station (ISS), the water on board has to be recycled to reduce the need for resupply from Earth;
Chemical and/or biological contamination can occur during the water recovery/treatment process, therefore the quality of the water needs to be periodically monitored to ensure crew safety;
Only basic measurements can be performed onboard the ISS, and full chemical characterization is usually carried out in sample returned to Earth;
Iodine (I2) is currently added to the water system as a biocide in the U.S. segment of the ISS.
Introduction
Credit: NASA

## Slide 3
A biocide needs to be added to the potable water onboard the ISS to prevent bacterial growth and make it safe for astronaut’s consumption;
Iodine has been successfully used for water disinfection on Earth and it is the biocide currently in use onboard the ISS;
Although iodine is essential in the human diet it can have adverse effects on the thyroid at elevated levels;
Iodine has to be removed prior to water consumption by the astronauts, adding complexity to the water processing system;
Ionic silver (Ag+) has been proposed as a new biocide to treat the water in the ISS and also future human space exploration vehicles/habitats. Ag+ is effective as biocide in levels (200 to 500 ppb) safe for human consumption.
Problem Description
Goal: To develop a method/technique for monitoring Ag+ levels in water ranging from 50 to 1000 ppb.

## Slide 4
Methodology
A capillary electrophoresis instrument with a contactless conductivity detector (CE-C4D) was used.
CE-C4D is an ideal method for measuring inorganic ions. It provides short analysis time, low sample and reagents consumption, and it can be automated and miniaturized.
Two methods were developed for monitoring Ag+ in water.
The methods were evaluated by analyzing a simulant of ISS water containing inorganic ions commonly present in the water: K+, Ca2+, Na+, Mg2+, Ni2+, and Zn2+.

## Slide 5
Results
Method 1
Medium: 5 M acetic acid
Limit of detection for Ag+: 100 ppb
Analysis time: 4.5 min
Allows simultaneous measurements of other cations commonly found in the ISS potable water.
Method 2
Medium: 0.5 M acetic acid
Limit of detection for Ag+: 25 ppb
Analysis time: 2.5 min
Allows detection of lower levels of silver in water but the other ions cannot be separated and quantified.

## Slide 6
Publications and Acknowledgements
This research was carried out at the Jet Propulsion Laboratory, California Institute of Technology, under a contract with the National Aeronautics and Space Administration.
Financial support for this project was provided by The Planetary Instrument Concepts for the Advancement of Solar System Observations Program.